## Slide 1
History of Land Subsidence in Tokyo
Shibaura Institute of Technology
Vice President
Masaru MORITA
Introduction
High Economic Growth Period and Land Subsidence
Environmental Problems due to Land Subsidence
Countermeasures against Land Subsidence
Conclusion
1

## Slide 2: Introduction
23 ward area
Tama area
「東京都総合地盤図（Ⅱ）」に加筆
Musashino upland
Tokyo lowland
Tama hill
Tokyo Bay
Tokyo Metropolis
N
Land Subsidence
lowland
hill
2

## Slide 3
1890
1915
1940
1965
2015
1990
0
5
4
3
2
1
year
Cumulative subsidence : m
Historical Process of
Land Subsidence
in Tokyo
3

## Slide 4
4
Nerima ward
Itabashi ward
Kita
ward
Adachi ward
Ayase
River
Chiba Prefecture
Edogawa River
Katsushika ward
Percentages of Areas by Ground Level
Toshima ward
Bunkyo ward
Taito ward
Arakawa ward
Sumida-ku
Shinnaka
River
Koto ward
Arakawa River
Naka River
Kyuedo River
LEGEND
Areas above high water level, but under threat of high-tide
Areas below high water level
Areas below low water level
Sumida River
Minato ward
Chiyoda ward
Minato ward
Meguro ward
Shinagawa ward
Ota ward
Kanagawa Prefecture
Setagaya ward
Equal or Lower than A.P. ± 0m
Equal or Lower than A.P. 2m
Higher than A.P. 5m
Equal or Lower than A.P. 5m
Total Area of Tokyo 23 wards: 623.0㎢ (2013)
Kita-ku
Arakawa-ku
Adachi-ku
Katsushika-ku
Misato
City
Matsudo
City
kyu-Edogawa river
Shin-Nakagawa river
Nakagawa river
Arakawa river
Kyu-Nakagawa river
Yokojyukkengawa river
Oyokogawa river
Sumidagawa river
Shinkansen
Yamanote plateau
W.L.. at high tide
plan high-tide level
W.L.. at normal tide
average high tide level
Edogawa ward
“Tokyo Zero Meter Area”
Most of the Tokyo lowland area is lower than the average high tide level.
Tokyo zero meter area is prone to storm surge damage and difficult to drain the inundation water from the area.
Once a destructive earthquake would hit the area and destroy the coastal dikes, the sea water would flow into the area and bring the huge inundation damage.

## Slide 5
1890
1915
1940
1965
2015
1990
0
5
4
3
2
1
year
Cumulative subsidence : m
High Economic Growth Period (1955 – 1973)
After the Second World War, Japan economy had the high economic growth period.
Industry had been rapidly growing and the population had been concentrated into the major cities , especially into Tokyo area.
This rapid increase in the number of factory and in population naturally demanded huge amount of industrial and domestic water in urban areas.
Private companies for industrial water and local governments for domestic water resumed their groundwater exploitations more intensively than before.
However they had learned that groundwater overwithdrawal causes serious land subsidence.
LAND SUBSIDENCE AGAIN !!
5

## Slide 6
Distribution of pumping wells
A huge amount of deep wells were drilled for industrial water by the private companies in the Tokyo lowland area during the period from 1950s to 1960s.
Groundwater Exploitation in Tokyo lowland Area
「地盤沈下と工業用水法」
(蔵田延男）昭和４６年
より
This groundwater exploitation brought about the groundwater level drop and serious land subsidence.
6

## Slide 7: Land Subsidence in Tokyo Lowland Area
Arakawa downstream area
遠藤毅「荒川下流域における地盤沈下の展開とその社会的背景」（荒川下流誌・２００５）より
The cumulative land subsidence during the period of 40 years from 1938 to 1977
Almost the whole area of the lowland have the subsidence over 1 m.
There should be serious land subsidence area in the eastern part of Koto ward with the cumulative subsidence over 3 m.
Contour line of cumulative land subsidence
Unit: cm
Tokyo Bay
7

## Slide 8
Damage of Land Subsidence
The house has leaned slightly because of land subsidence.
Ships could not go through under the bridge owing to the land subsidence.
8

## Slide 9
Damage of Land Subsidence
The ground surface is lower than the sea level.
Uprise of Building
9

## Slide 10
Loam - clay
Sand Gravel
Clay
Mudstone
Upland
Lowland
Sand
Loam
Alluvial
Diluvial
Tertiary
Loam - clay
Sand Gravel
Clay
Mudstone
Benchmark
Observation
Well
Two Type s of Land Subsidence
Surface Layer Subsidence
Deep Layer Subsidence
Alluvial Layer
Diluvial Layer
10

## Slide 11
Overpumping
Shrinkage
Protruding
Aquiclude (clay)
Confined Aquifer
Squeeze
Groundwater Flow
PUMP
Land Subsidence
Overpumping
Groundwater level drop
Squeeze of water in aquiclude
Shrinkage of aquiclude
Land subsidence
Mechanism of Land Subsidence (Surface layer subsidence)
11

## Slide 12
Over the sunken area, old well casing has gradually risen above the ground surface.
This suggests that the sinking is caused by consolidation distributed throughout the layer penetrated by wells.
“Protruding” Well as an Evidence of Surface Layer Subsidence
Old ground surface
Present ground surface
Shrinkage of surface layer
Old ground surface
Present ground surface
Shrinkage of surface layer
12

## Slide 13
Physical Damage from Surface Layer Subsidence
Uprise of building
Leaning of house
prone to inundation
Settlement
of dike and levee
Collapse of
underground facilities
Land subsidence
Support layer
Surface Layer subsidence caused visible damages :
Uprise of buildings
Leaning of house
Collapse of underground facilities
Cracks of buildings and houses
Settlement of dike and levee
Increasing the inundation prone area
13

## Slide 14
From Surface Layer Subsidence
to Deep Layer Subsidence
1960
1970
1980
1985
1955
1965
1975
Shrinkage A
(0m < depth <70m)
Shrinkage B
( depth >70m)
Shrinkage A + B
Shrinkage of layer ( cm )
Minamisuna No.1 Observation Well (Koto-ku)
sand gravel
clay
sand
sand /sand gravel
clay
sand
sand
Sand gravel
Alluvial
Deposit
Diluvial
Deposit
Depth (m)
Soil Type
Surface
14

## Slide 15
Physical Damage from Deep Layer Subsidence
Deep Layer subsidence caused invisible damages :
prone to inundation
prone to storm surge
Settlement
of dike and levee
Land subsidence
Support layer
Increasing the inundation prone area
Increasing the storm surge prone area
15

## Slide 16
Industrial Water Law
Alternative Source of Water Use
Countermeasures against Land Subsidence in Tokyo
16

## Slide 17
Enactment of law which aims to reduce the amount of groundwater pumping
Designation of the areas where the permission standard of the law should be applied for the groundwater withdrawal reduction
Prohibition of groundwater exploitation with new pumping wells unsatisfactory to the standard of the law
Prohibition of using the existing wells unsatisfactory to the standard of the law through the development of alternative water resources (e.g. treated sewage water or river water).
*standard of the Law : strainer depth and cross sectional area of discharge outlet
Industrial Water Law(1956)
for Tokyo Lowland
>> National Government
>> Prefectural Government (local government)
17

## Slide 18: Groundwater Withdrawal Regulations and Groundwater Level Rise
Groundwater level
Industrial Water Law worked effectively to raise the groundwater level owing to the development of alternative water resources.
Groundwater level : m (T.P.)
Groundwater withdrawal : 104 m3/day
Regulation for Koto Area
Regulation for Johoku Area
Koto
Well
Groundwater Level
Groundwater Pumping
Adachi
Well
Edogawa
Well
18

## Slide 19: Groundwater Withdrawal Regulations and Land Subsidence
Owing to the regulations of groundwater withdrawal, the groundwater levels went up clearly.
However, the ground surface never recovered to the original level with a very slight rebound.
The ground surface sank over 4 m in Koto ward.
We should know that the land subsidence could never recover even if we would prohibit the groundwater pumping.
19

## Slide 20
Why did the Tokyo Area succeed in stabilization of land subsidence?
The main cause of the land subsidence was the overwithdrawal of groundwater for industrial water use. The industrial water was the most demanded during the high economic growth period.
The Industrial Water Law was efficiently applied to the factories located in the Tokyo lowland area that suffered from the land subsidence.
It is difficult to restrict the water use for domestic and agricultural purposes. Because there are no laws to restrict domestic and agricultural water use.
The alternative water sources, recycled water and river water, were efficiently introduced to the industrial areas.
The factories were forced to move away from the industrial area owing to the three laws related to the factory location.
>> Accumulation of the geologic data and monitoring system of groundwater level and land subsidence
20

## Slide 21
Conclusion - Countermeasures against Land Subsidence
21
Mitigation
Adaption
Monitoring
Management
Regulations by law, ordinance, administrative guidance
Alternative water resources development
Effective water use – Water supply system improvement
Raising of coastal dikes and river levee
Raising of ground level
Flood inundation prevention
Level survey
Groundwater level observation
Investigation of groundwater use
Optimal groundwater use and conservation of groundwater resources